## Slide 1
ELG 5163 – Machine Vision
Project Presentation
Inter-vehicle distance estimation using displaced stereoscopic vision
Presented by: Alfa Budiman, Mathieu Falardeau Date: 31/03/2022
uOttawa.ca
Faculté de génie | Faculty of Engineering
Notes: PAGE COUVERTURE (option 1) ÉBAUCHE (DOCUMENT NON FINALISÉ) À lire avant d’utiliser le gabarit
NOTE : Les éléments du gabarit suivants ne peuvent être modifiés : • Entête organisationnelle grenat (Université d’Ottawa | University of Ottawa) • Pied de page organisationnel comprenant la bande grise et violet foncé ainsi que le logo, à l’exception de l’adresse Web qui peut être modifiée en suivant les étapes suivantes : dans le document PowerPoint, cliquez sur l’onglet View, puis sélectionnez Slide Master. Sur le menu d’affichage (à gauche), sélectionnez la troisième diapositive et inscrivez la nouvelle adresse sur celle-ci.
COVER PAGE (option 1)
DRAFT ONLY (FILE NOT FINAL) Read before using template
NOTE: The following elements of the template should remain untouched and cannot be modified:
• Corporate (Université d'Ottawa | University of Ottawa) garnet header
• Corporate uOttawa footer including the grey/dark purple stripe and logo, with the exception of the URL which can be customized to a specific URL by following these simple steps: On the PowerPoint View tab, in the Master Views group, select Slide Master. Select the third slide on the left side panel, and type in the desired URL on the slide.

## Slide 2
Mathieu Falardeau mfala097@uottawa.ca
Alfa Budiman abudi097@uottawa.ca
1

## Slide 3: Aim
2
Present our ELG 5163 Machine vision term project and provide insight on a different approach to the traditional stereoscopic vision.

## Slide 4: Outline
Introduction
Problem Description
System Description
Methodology:
  Object Detection
  Direction Calculation
  Distance Calculation #1
  Distance Calculation #2
Test & Results
Discussion and Conclusion
3

## Slide 5: Introduction

## Slide 6: Methodology
Object Detection and Feature Matching
  Detect red pixels on burgerbot and black pixels on wafflebot
Direction Calculation
  Calculate relative direction from respective cameras
Position Calculation
  Quadcopter and wafflebot positions are known
  Relative directions to burger bot are known
  Complete triangle to find position of burgerbot
Distance Calculation
  Difference between wafflebot and burgerbot positions
3
Notes: 1 min,
Go over 4 step process of vision based distance estimation
Step 1 – object (a red burgerbot) is observed, detected and tracked from 2 cameras, one overhead on a quadcopter, and one mounted on a wafflebot.
Step 2 - the direction to the object from both observers is estimated as a unit vector by using the pixel coordinates of detected object
Step 3 – with the positions of observers known and direction (unit vector) to object known, the position of the object can be calculated
Step 4 – the distance from the observers to the object is the difference between their positions

## Slide 7: Object Detection and Feature Matching
Quadcopter camera
Wafflebot camera
Notes:   Object detection and feature matching
  Quadcopter camera detected groups of black pixels and red pixels
  Center of black pixels is wafflebot. Red pixel closet to center of black pixels is burgerbot
  Wafflebot camera detected red pixels. Center of red pixels is burgerbot.

## Slide 8: Methodology
Direction Calculation
3

## Slide 9: Distance Calculator 1
Ideally these lines would intersect but due to imperfection of feature matching process, their perfect intersection is extremely unlikely.
Satisfying these conditions solves for scalar parameters s and k that yield closest points on two non-intersecting lines:
Notes: 1 min 30 ish ish

## Slide 10: Methodology
3
Distance Calculator 2

## Slide 11: Test Drive
Burgerbot drove through 4 waypoints under observation from quadcopter and wafflebot.
Test 1 – stationary observer. Test 2 – leader / follower. Same burgerbot path in both tests
3
Notes: 1 min ish

## Slide 12: Test Drive - Stationary
3
Notes: 1 min ish

## Slide 13: Test Drive – Leader Follower
3
Notes: 1 min ish

## Slide 14: Results and Discussion
Stationary Test
  Image of path here
3
Notes: - Good distance measurement between both vision based methods compared to lidar

## Slide 15: Results and Discussion
Leader / Follower Test
3
Notes: Distance measurement is good but starts to deviate when the wafflebot starts moving to catch up to the burgerbot
Error is less when wafflebot is stationary, which occurs when it is rotating to orient itself to face the burgerbot

## Slide 16: Discussion
Applications:
  Multi-robot path planning
  Leader follower with obstructing obstacles
  Distance measurement over uneven terrain (hills)
Further improvement
  Improve robustness of object detection
  Improve robustness of feature matching
  Detection of different object types
3

## Slide 17: Conclusion
Vision from a UGV and a UAV was combined to measure distance between a UGV and a moving object.
Effective for stationary UGV.
Requires further development on object detection and feature matching.
3